SALTRO TPC readout system Presented by  Ulf Mjörnmark Lund University
SALTRO TPC readout system
Presented by
Ulf Mjörnmark
Lund University

---
Overview of current design
The Front End Multi Chip Module (MCM)
Low Voltage (LV) system
Detector Control System (DCS)
Scalable Readout Unit (SRU) & Trigger & Power Pulsing
DAQ system
Status & Time scale

---
Overview
LCTPC
ENDPLATE
7 pad plane
modules
Front End = 25
MultiChipModules
connected on
a pad plane =
3200 channels
* 3 pad planes
FRONT END
18 cm
SRU =
Scalable
Readout
Unit
(RD51)
CONTROL
TRIGGER
DAQ/Monitor
1

---
Multi Chip Module (MCM)
Current:
FEC = 8 ALTRO + 8 PCA16
128 channels
Parallel readout bus
17*18 cm
FPGA board controller
Multi Chip Module (MCM) = 8 SALTRO
128 channels
Serial readout
2.5*3.5 cm
CPLD (firmware Brussels)
“same” except Low Voltage
Untested &
Unpackaged chip
Bonded on Carrier
Test (unknown yield)!
BGA on main board
With industry
Component placement
Side view

---
Low Voltage Card
5 MCM * 8 Voltages = 40 regulators
Control of individual regulator
On/off
Monitor on each Low Voltage card
48 voltages
40 currents
1 temperature
On each MCM
1 temperature
1 DAC
MCM1
MCM2
MCM3
MCM4
MCM5
5 low voltage cards and
~700 settings/values per pad plane
Detector
Control
System
NEED

---
Detector Control System
In control room
Display/Logging/Control:
DOOCS (used at DESY)
(Distributed Object Oriented Control System)
Disable Run if problem
STOP TRIGGER/DAQ/ALARM
How?
WANTED
Near electronics
Standalone Monitoring
Automatic power off!
Low Voltage Board
370 W >>> power pulsing
110 W (regulators) cooling?
260 W CO2 cooling (Japan)

---
DAQ system – preliminary!
7

---
Local - Common DAQ interface
Scheleton: provided by common DAQ, calls to user routines
Interface: well defined protocol, user implements code
WANTED
8

---
Trigger signal usage
Clock	Synchronous. Stability, jitter...? Frequency?
20/40 Mhz for sampling. 160 Mhz for data transfer
Trigger	Prompt, fanout to
→ SRU (and DAQ computer?), time stamp of event
→ sampled by Front End, for precise time when “particle	passed the detector”
Busy	from SRUs and DAQ computer. SRUs can be daisy chained
Spill	for Power Pulsing (power off SALTRO outside spill)
Takes 100 microsec to power on! No triggers during that time!
Do one need a signal (hw/sw?) telling if system is in power	pulsing mode, powered up/down?
Trigger	distribute to SRUs. Broadcast
number
WANTED
9

---
Aim of a common Trigger & DAQ system
for AIDA and what comes after (AfterAIDA)
Run	Data files	Detector
Trigger	Control	Common	Merge	Monitor	control
AIDA
Common DAQ	yes	yes	(yes)	yes	-	-
Local DAQ
Common	yes	yes	-	-	-	-
Local	-	yes	yes	-	yes	yes
AfterAIDA
Common DAQ	yes	yes	yes	yes	yes	yes
Local DAQ
Common	yes	yes	yes	-	yes	yes
Local	-	-	-	-	-	-
AfterAIDA => “standardized modular open source” Trigger & DAQ
for all ILD activities (i.e. easy to compile/implement/understand/add
code on all systems ….)
10

---
STATUS
Multi Chip Module
SALTRO - 600 untested naked chips exist
Carrier board - design ready and PCBs delivered
Industry collaboration for bonding/mounting
Prototype MCM to be produced (with one packaged SALTRO)
Firmware started to be developed in Brussels
Low Voltage board
Design ready
Prototype board is being tested
Detector Control System
Hardware - design ready and hardware made, tested and working
Firmware – in progress, mostly done
DOOCS – not yet done anything
Trigger/DAQ
Bought one SRU – sent to Brussel for tests and development of firmware
Trigger/Power pulsing/DAQ hard/software – adopt ALTRO EUDET DAQ: replace
ALICE DDL with ethernet readout. Issues: transfer rate, data size, trigger rate.
MicroTCA? Still to be defined and done
Time
2014: emphasis on electronics, software as needed for this
2015: full setup