## Slide 1
Accelerator Cryogenics
An Introduction
J. G. Weisend II
Deputy Head of Accelerator Projects
Adjunct Professor, Lund University
November 14, 2014

## Slide 2: Outline
Introduction
Production of Cold
  Refrigerators & liquefiers
  Carnot efficiency
  Coefficient of performance
Maintenance of Cold
  Cryostats and cryomodules
  Basic heat transfer mechanisms and guidelines for design
  Example cryostat (ESS Elliptical cavity CM)
Summary

## Slide 3: Introduction
Cryogenics : the science and technology of phenomena occurring below 120 K
Cryogenics plays a major role in modern particle accelerators
  Enables superconductivity
    Beam bending and focusing magnets (1.8 K – 4.5 K)
    Magnets for particle identification in large detectors (4.2 – 4.5 K)
    Superconducting RF cavities for particle acceleration (1.8 K – 4.2 K)
  Allows dense pure liquids
    LAr calorimeters (87 K)
    LH2 moderators, targets and absorbers (20 K)

## Slide 4: Introduction
Since the Tevatron (1983) accelerator cryogenic systems have become larger, more reliable, more efficient, industrialized and much more widespread
Cryogenics is found in all types of accelerator applications including: HEP accelerators, light sources, heavy ion machines, neutron sources and ADS
This lecture will give an overview including examples of several key aspects of cryogenic engineering related to accelerators. But there is much more to learn.
I will discuss how we get equipment to cryogenic temperatures and keep it at those temperatures in accelerators.

## Slide 5: Introduction
LHC
Magnets
SNS
4 K
Cold
Box
ESS Cryomodule

## Slide 6: Introduction
ATLAS
Magnets
At CERN
JSNS LH2 Moderator (6.5 kW @ 16 K)

## Slide 7: Catching Cold
There are really only a few ways in which to make a pure fluid such as helium colder
  Cause the fluid to do work by making it expand against a piston or turbine while keeping it thermally isolated from the outside environment Isentropic Expansion
  Transfer heat from the fluid to a colder surface
  Cause the fluid to do “internal work” by expanding it through a valve while keeping it thermally isolated Isenthalpic Expansion or Joule-Thomson expansion
  Once the fluid is a liquid, reduce the pressure above the fluid below atmospheric pressure thus reducing the saturation temperature
All modern cryogenic plants do the first 3. Ones that provide cooling below 4.2 K also do the last item

## Slide 8: Collins Cycle
Cycle consists of :
  1) Compression of Helium to ~ 16 Bar with cooling back to 300 K + oil removal
  2) Cooling of high pressure gas with LN2
  3) Isentropic expansion via 2 or more expansion engines
  4) Cooling of high pressure gas by the cold returning low pressure stream
  5) Isenthalpic expansion through JT valve
  6) Return of gas to compressors at just above 1 Bar

## Slide 9: CTI 4000 Refrigerator (early 80’s vintage ~ 1.2 kW @ 4.5 K)

## Slide 10: LHC 4.5 K Refrigeration Plant 18 kW @ 4.5 K – produced in ~ 2004 1of 8 required (4 from Linde, 4 from Air Liquide)
Note:
Large number of expansion turbines – some in series with HP stream
Medium pressure return
Heat loads at intermediate temperatures

## Slide 11: Carnot Cycle
This is an ideal cycle: all processes are reversible
  Entropy is only changed by absorbing or removing heat at constant temperature
  2nd law of Thermodynamics, in a reversible process dQ = -TdS
The Carnot Consists of 4 steps
  Compress the working fluid isothermally at TH (1-2)
  Expand the working fluid isentropically from TH to TC (2-3)
  Absorb heat into the working fluid isothermally and reversibly at TC (3-4)
  Compress the working fluid isentropically from TC to TH (4-1)
  Note isentropically = reversibly and adiabatically

## Slide 12: Carnot Cycle
How do we describe the performance of such a cycle?
S
1
2
3
4
TH
TC
Q
s1
s2

## Slide 13: Coefficient of Performance & the Carnot Cycle
Coefficient of Performance: the heat absorbed from the cold sink divided by the net work required to remove this heat
  Minus sign takes into account that the heat absorbed by the cycle is positive while the work done is negative
Since this is a closed cycle, the net work done is equal to the net heat transferred. Since this cycle completely reversible, the 2nd law gives the net heat transferred as:

## Slide 14: Coefficient of Performance & the Carnot Cycle
Thus
Again from the 2nd Law:
Thus, for the Carnot cycle the COP may be written as:
  For the Carnot cycle the COP is dependent only on the temperatures

## Slide 15: Coefficient of Performance & the Carnot Cycle
For a plant operating between room 300 K and 4.2 K, the Carnot COP is 4.2/( 300 – 4.2) or 0.0142
The Carnot cycle is the ideal case. It is the best you can do without violating the laws of thermodynamics
Note that the form of the Carnot COP shows that you have a better COP (thus a more efficient process or refrigerator) if TC is large
  It is always thermodynamically more efficient to intercept heat (provide cooling) at higher temperatures
  This fact drives a lot of cryogenic design
In practice, we generally discuss the inverse of the COP because this allows us to describe the number of watts of work required to provide 1 Watt of cooling at a given temperature. For a Carnot cycle providing cooling at 4.2 K. This is 70 W/W
  People will frequently and incorrectly refer to this as a COP as well

## Slide 16: Carnot Cycles & the Real World
Can we build a real machine using a Carnot cycle? In a word NO
Why?
  Compressing a fluid isothermally is very hard to achieve, Normally the fluid is compressed and then cooled back down to 300 K
  Expanding or compressing fluid isentropically is basically impossible
  We can absorb heat into a boiling fluid isothermally but not with out irreversible losses
How close can we get to Carnot? We define the Figure of Merit (FOM) as:
  We also speak in terms of “percent Carnot” i.e. FOM of 0.2 is 20% Carnot

## Slide 17: The real world is sometimes not kind to cryogenic engineers
These are state of the art helium refrigerators. Note that the best of them (for LHC) runs at about 220 W/W or a FOM of 0.318 or at 32% Carnot

## Slide 18
Oil
cooler
Compr. motor
Middle temperature Return
Middle temperature Supply
Oil vessel
Helium compressor
Helium cooler
He to fine oil removal
He from cold box
High temperature Return
Middle temperature Return
25C
25C
27C
27C
27C
39C
85C
85C
90C
32C
90C
32C
83C
37C
ESS Cryoplant Energy Recovery

## Slide 19: Cryostats, Cryomodules and Dewars
What is a cryostat?
  A device or system for maintaining objects at cryogenic temperatures.
Cryostats that contain SCRF cavity systems are also frequently called cryomodules
Cryostats whose principal function is to store cryogenic fluids are frequently called Dewars. Named after the inventor of the vacuum flask and the first person to liquefy hydrogen

## Slide 20: Cryostats
Cryostats are one of the technical building blocks of cryogenics
Cryostat design involves many subtopics most of which we don’t have time to cover here:
  Development of requirements
  Materials selection
  Thermal insulation
  Support systems
  Safety
  Instrumentation
One of the best ways to learn about cryostat design is through examples
There are many different types of cryostats with differing requirements
  The basic principles of cryostat design remain the same
  Before we can do anything else we have to define our requirements

## Slide 21: E158 LH2 Target Cryostat

## Slide 22: Cryostat Requirements
Maximum allowable heat leak at various temperature levels
  This may be driven by the number of cryostats to be built as well as by the impact of large dynamic heat loads (SCRF or target cryostats)
Alignment and vibration requirements
  Impact of thermal cycles
  Need to adjust alignment when cold or under vacuum?
  Alignment tolerances can be quite tight (TESLA :
  +/- 0.5 mm for cavities and +/- 0.3 mm for SC magnets)
Number of feed throughs for power, instrumentation, cryogenic fluid flows, external manipulators

## Slide 23: Cryostat Requirements
Safety requirements (relief valves/burst discs)
  Design safety in from the start. Not as an add on
Size and weight
  Particularly important in space systems
Instrumentation required
  Difference between prototype and mass production
Ease of access to cryostat components
Existing code requirements (e.g. TUV or ASME)
Need, if any, for optical windows
Presence of ionizing radiation

## Slide 24: Cryostat Requirements
Expected cryostat life time
Will this be a one of a kind device or something to be mass produced?
Schedule and Cost
  This should be considered from the beginning
  All Design is Compromise

## Slide 25: Thermal Insulation
This is key to proper cryostat design
The effort and cost expended on this problem are driven by cryostat requirements:
  Dynamic vs. static heat loads
  Number of cryostats
  Operational lifetime & ability to refill cryostats (e.g. space systems)
Lowest possible static heat leak isn’t always the best answer
It is thermodynamically best to intercept heat leaks at the warmest temperature practical

## Slide 26: Three Ways to Transfer Heat
Conduction
  Heat transfer through solid material
Convection
  Heat transfer via a moving fluid
    Natural or free convection – motion caused by gravity (i.e. density changes)
    Forced – motion caused by external force such as a pump
Radiation
  Heat transferred by electromagnetic radiation/photons
There is no such thing as a perfect insulator – though we can design systems with very small heat leaks
All matter above 0 K radiate heat

## Slide 27: Conduction Heat Transfer
Fundamental Equation – The Fourier Law in one dimension
If we assume constant cross section we get:
Reduce conduction heat leak by:
  Low conductivity material: make K(T) small
  Reduce cross sectional area: make A small
  Increase length: make L large
  For a given TC make TH smaller: i.e. use intermediate temperature heat intercepts

## Slide 28: Design Example ILC Cryomodule Support Post
Total Heat Leak (conduction & radiation)
  70 K - 10.5 W
  5 K - 0.9 W
  2 K - 0.03 W
Can support up to 50 kN
300 K
70 K
4 K
2 K
Fiberglass pipe
Courtesy T. Nicol - Fermilab
G-10 Tube
300 K
80 K
5 K
2 K

## Slide 29: Convection Heat Transfer
Fundamental Equation: Newton’s law of cooling
Q = hA(Tsurface – Tfluid)
where h is the heat transfer coefficient and is a function of Re, Pr, geometry etc depending on the situation
In cryogenics we eliminate convection heat leak in cryogenic systems by “simply” eliminating the fluid – vacuum insulation
Using vacuum insulation to create vessels capable of storing cryogenic liquids was first done by James Dewar – who liquefied hydrogen

## Slide 30: Vacuum Insulation
How much vacuum is enough?
  This of course depends on the heat leak requirements but generally we want to be below 10-5 mBar If we maintain this level or better we can generally neglect the convection heat leak for most applications.
Cryopumping
  At cryogenic temperatures almost all common gases condense and freeze onto the cold surface. Typically, we’ll see that once surface are cooled to ~ 77 K the isolation vacuum will drop to the 10-8 mBar or better range if the system is leak tight and doesn’t have significant outgassing

## Slide 31: Radiation Heat Transfer
Frequently the largest source of heat leak to cryogenic systems
Fundamental Equation: Stefan-Boltzmann Law – energy emitted from an ideal black body: Eb = sT4 where s = 5.67x10-8 W/m2K4
  Real world Assumptions:
    Emissivity (e) << 1 and independent of wavelength (grey body)
    Two parallel infinite plates: Radiative heat flux (W/m2)
    Eq. A
    Frequently in cryogenic systems e1 ~ e2 << 1 then Eq. A becomes:
    Eq. B

## Slide 32: Radiation Heat Transfer
    Two long concentric cylinders or concentric spheres (1 represents the inner cylinder): the radiative heat flux (W/m2) on the inner cylinder is
    Eq. C
    Note as is frequently the case in cryogenics, if the spacing between the cylinders is small compared to the inner radius (i.e. A1 ~ A2 ) Eq. C becomes Eq. A

## Slide 33: Radiation Heat Transfer
Looking at Eq. A, How do we reduce the radiation heat transfer?
We could reduce the emissivity (e)
  This is done in some cases; using either reflective tape or silver plating
  Better below 77 K
  It’s also part of MLI systems (see below)
  We have to consider tarnishing
  May be labor intensive
From Helium Cryogenics – S. W. Van Sciver

## Slide 34: Radiation Heat Transfer
Another way to reduce radiation heat transfer is to install intermediate actively cooled radiation shields that operate at a temperature between 300 K and the lowest cryogenic temperature. This has several advantages.
  It greatly reduces the heat load to the lowest temperature level
    Assume parallel plates with e = 0.2
    then from Eq. B q ( 300 K – 4.2 K ) = 46 W/m2 while q (77 – 4.2) = 0.2 W/m2
  It allows heat interception at higher temperatures & thus better Carnot efficiency
  Such an actively cooled shield provides a convenient heat intercept for supports, wires etc to reduce conduction heat leak.
Shields may be cooled by
  Liquid baths ( LN2)
  Vapor boil off from stored liquid – common in LHe storage dewars
  Cooling flows from refrigeration plants
  Conductive cooling via small cryocoolers

## Slide 35: Radiation Heat Transfer
Use Multilayer Insulation (MLI) or “superinsulation” inside the vacuum space to reduce heat leak

## Slide 36: Multilayer Insulation
Used in almost all cryostats
Consists of highly reflective thin sheets with poor thermal contact between sheets
Don’t pack MLI too tightly. Optimal value is ~ 20 layers / inch
Great care must be taken with seams, penetrations and ends.
  Problems with these can dominate the heat leak

## Slide 37: Example of MLI in LHC Magnets
“SERIES-PRODUCED HELIUM II CRYOSTATS FOR THE LHC MAGNETS: TECHNICAL CHOICES, INDUSTRIALISATION, COSTS” A. Poncet and V. Parma Adv. Cryo. Engr. Vol 53

## Slide 38
How Are These Principles Used on
the ESS Elliptical Cryomodule Design ?
total length: 6.6 m
Beam height: 1.5 m
Similar to CEBAF/SNS cryomodule with 4 cavities per cryomodule
Common design for medium (6 cells) and high beta (5 cells) cavity cryomodules
Accelerating gradient:
  for b=0.67 (Medium Beta): Eacc=16.7 MV/m Qo> 5E9 at 2 K
  for b=0.86 (High Beta): Eacc=19.9 MV/m Qo> 5E9 at 2 K
Maximum operating helium pressure: 1.431 bar
Courtesy P. Bosland CEA

## Slide 39: There is Much More to Cryogenic Engineering
This has been just a small sample of cryogenic engineering as applied to accelerators. Other topics include:
  Properties of Cryogenic Fluids
  Cryogenic Properties of Materials
  He II (superfluid helium)
  Safety in Cryogenics
  Instrumentation
  Cryogenic Distribution Systems
  Cryogenics below 1 K
  Use of Small Cryocoolers
  Vacuum Systems
  High Temperature Superconductor Applications
  Superconducting Magnets and RF Cavities

## Slide 40: The Use of Cryogenics in Accelerators is Growing
More than 17 current accelerators use cryogenics in some form and an additional 15 new accelerators using cryogenics are planned between now and 2025 in a wide range of locations: Europe, India, China, Korea, Brazil, USA, Japan
These future accelerators include some very large installations: FAIR, XFEL, ESS, LCLS II, ILC
The need for trained staff in this area is an issue and Lund University is in the early stages of developing a center of excellence in cryogenics including classes (senior undergraduate/graduate), research projects and collaborations with ESS and possibly Maxlab

## Slide 41: Examples of Operating Facilities
Name | Type | Lab | T (K) | Refrigeration Capacity | Comments
LHC | Accelerator CMS ATLAS | CERN | 1.9 4.5 4.5 40/80 80 | 8 plants ea 2.4kW @ 1.9K 1.5 kW @4.5 K 6 kW @ 4.5K 20 kW @ 40 – 80 K 20 kW @ 80 K | Each plant has 18 kW capacity eqv. @ 4.5 K LAr calorimeter
CEBAF/12 GeV | Accelerator | JLab | 2.1 | 8.4 kW @ 2.1 K | 
JSNS | H2 Moderator | J-PARC | < 20 | 6.5 kW @ 15.6 K | 
SNS | Accelerator H2 Moderator | ORNL | 2.1 20 | 2.4 kW @ 2.1 K 7.5 kW @ ~ 20 K | 
S-DALINAC | Accelerator | TU Darmstadt | 2.0 | 120 W @ 2.0 K | 
FLASH | Accelerator | DESY | 2.0 |  | TESLA tech
RHIC | Accelerator | BNL | 4 | 24.8 kW @3.8 K plus 55 kW @55K | 
ARIEL (e linac) | Accelerator | TRIUMF | 2.0 | 288 L/h | 

## Slide 42: Examples of Future Facilities
Name | Type | Lab | T (K) | Refrigeration Capacity | Status (Start of Operation)
ESS | Accelerator LH2 moderator Instrum. supply | ESS | 2.0 40/50 16 4.2 | 3 kW 11 kW 25 kW 7500 l/month | Construction (2019)
ERL | Electron Linac | Cornell | 1.8 5 40-50 | 7.5 kW @ 1.8 K 6.8 kW @ 5 K 144 kW @ 40-80 | Proposed: Prototypes under construction TESLA Tech
XFEL | Electron Linac | DESY | 2.0 5 – 8 40-80 | 2.5 kW @ 2 K 4 kW@ 5 -8 K 26 kW @ 40-80 K | Construction (2017) TESLA Tech
LCLS II | Accelerator | SLAC | 2.1 K | ~ 4 kW @ 2.1 K | Construction (2019) TESLA Tech
FAIR | Accelerator & separator magnets | FAIR/GSI | 4 50-80 | Up to 37 kW@ 4 K Up 30 kW @ 50- 80 K | 2 Plants Construction ( 2019)

## Slide 43: Summary
Cryogenics is an enabling technology in modern particle accelerators
Cryogenics is a multidisciplinary field using many aspects of physics and engineering
The use of cryogenics in accelerators (as well as in other scientific research fields) is growing and additional talent is needed.
ESS and Lund University are working together to develop a center of excellence in cryogenics in Lund

## Slide 44: Back Up Slides

## Slide 45: Refrigerators vs. Liquefiers
Refrigerators are closed cycle systems
  They provide cooling and can create liquids but all the mass flow is returned to the start of the cycle
  Such systems are said to have “balanced flow”
Liquefiers are open cycle systems
  They provide a liquid which is then drawn off and used elsewhere
  These have “unbalanced flows” the amount of mass returned to the start of the cycle is less than the amount that started by the mass that was converted to liquid.
  In order to keep the cycle running this mass would have to be added as room temperature gas.

## Slide 46: Refrigerators vs. Liquefiers
In practice, this distinction is less clear cut
  Modern cryogenic plants can operate either as refrigerators or liquefiers and in fact, generally operate as a mixture of the two.
  We talk about refrigeration loads & liquefaction loads
  A key issue is at what temperature is the boil off gas from a cryogenic liquid returned to the cycle?
    If brought back at a cryogenic temperature and used to cool incoming warmer gas then this is a refrigeration load
    If brought back warm and not used to cool incoming warmer gas this is a liquefaction load
The thermodynamic rules are the same for refrigerators and liquefiers